## Slide 1: CSCI3150 Introduction to Operating Systems
Lecture 13: File Systems
Part I: I/O Devices, HDD

## Slide 2: What problems are we solving?
Persistent data storage and access
Fast-growing industry
1956, IBM, 24 inches, 3.75MB, 1KB/sec, >$150k
2015, Seagate, 3.5 inches, 5TB, 6GB/sec, <$200

## Slide 3: History of storage technology
1956: IBM 350, 24 inches,
3.75MB, 1KB/sec, > $150,000
1980: IBM 3380, first GB
disk (1.26G), > $100K
1980: ST-560, first 5.25
inch drive, 5MB, $1500
Tape (DECtape): primary storage for
main-frames and mini-computers (1950 ~ 70s)
NextCom notebook 2006: first
laptop w/ SSD as storage

## Slide 4: History is heavy…
Source: https://en.wikipedia.org/wiki/File:SixHardDriveFormFactors.jpg/

## Slide 5: File systems: Agenda
First we will discuss “generic I/O devices and abstractions”…
… and properties of physical hard disks
Then we will discuss how we build file systems on them
  Files, directories
  Sharing, protection
  File system layout, design
  …

## Slide 6
I/O Devices

## Slide 7: I/O Devices
Input/Output, I/O, is critical to interact with computer systems
Issues:
  How should I/O be integrated into systems?
  What are the general mechanisms?
  How can we make it efficiently?

## Slide 8: Structure I/O Devices
CPU
Memory
NIC
Prototypical System Architecture
Memory Bus
(proprietary)
General I/O Bus
(e.g., PCIe)
Peripheral I/O Bus
(e.g., SCSI, STAT, USB)
CPU is attached to the main memory of the system via some kind of memory bus.
Some devices are connected to the system via a general I/O bus.

## Slide 9: I/O Architecture
Buses
  Data paths to enable information exchange between CPU, RAM, and I/O devices.
I/O bus
  Data path that connects a CPU to an I/O device.
  I/O bus is connected to I/O devices by three hardware components: I/O ports, interfaces and device controllers.
not this bus
PCIe

## Slide 10: Canonical Device
A Canonical Device has two important components.
  Hardware interface allows the system software to control its operation.
  Internals which are implementation specific.
Command
Data
Canonical Device
Registers:
Micro-controller (CPU)
Memory (DRAM or SRAM or both)
Other hardware-specific chips
Status
interface
internals

## Slide 11: Hardware interface of the canonical device
status register
  See the current status of the device
command register
  Tell the device to perform a certain task
data register
  Pass data to the device, or get data from the device
By reading and writing above three registers,
the operating system can control device behavior.

## Slide 12: Hardware interface of the canonical device (Cont.)
Typical interaction
while (STATUS == BUSY)
; //wait until device is not busy
write data to data register
write command to command register
(doing so starts the device and executes the command)
while (STATUS == BUSY)
; //wait until device is done with your request

## Slide 13: Polling
Operating system waits until the device is ready by repeatedly reading the status register.
  Simple; responsive
  However, it wastes (lots of!!) CPU time just waiting for the device
    Switching to another ready process is better in terms of utilizing the CPU.
.1 | 1 | 1 | 1 | 1 | p | p | p | p | p | 1 | 1 | 1 | 1 | 1
CPU
Disk
Diagram of CPU utilization with polling
1 | 1 | 1 | 1 | 1
: task 1
1
: polling
P
“waiting IO”

## Slide 14: Interrupts
Put the process waiting on I/O to sleep and context-switch to another
When the I/O finishes, wake up the sleeping process by interrupts
  Enable CPU and the disk to be better utilized
1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1
CPU
Disk
Diagram of CPU utilization with interrupts
1 | 1 | 1 | 1 | 1
: task 1
1
: task 2
2

## Slide 15: Polling vs interrupts
Interrupt is not always the best solution
  If, device performs very quickly, interrupts will “slow down” the system
  Because context switch is expensive (switching to another process)
If a device is fast  polling is better.
If it is slow  interrupt is better.

## Slide 16: CPU is once again over-burdened
CPU wastes a lot of time to copy a large chunk of data from memory to the device.
1 | 1 | 1 | 1 | C | C | C | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1
CPU
Disk
Diagram of CPU utilization
1 | 1 | 1 | 1 | 1
“over-burdened”
: task 1
1
: task 2
2
C
: copy data from memory

## Slide 17: DMA (Direct Memory Access)
Copy data in memory by knowing “where the data lives in memory, how much data to copy”
When completed, DMA raises an interrupt, I/O begins on disk
1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1
CPU
DMA
Diagram of CPU utilization by DMA
1 | 1 | 1 | 1 | 1
C | C | C
Disk
: task 1
1
: task 2
2
C
: copy data from memory

## Slide 18: Device interaction
How the OS communicates with the device?
Solutions
  I/O instructions: a way for the OS to send data to specific device registers.
    in and out instructions on x86
  memory-mapped I/O
    Device registers available as if they were memory locations.
    The OS load (to read) or store (to write) to the device instead of main memory.

## Slide 19: Device interaction (Cont.)
How the OS interact with different types of interfaces?
  build a file system that worked on top of SCSI disks, IDE disks, USB keychain drivers, and so on.
Solution: Abstraction
  Encapsulate specifics of device interaction

## Slide 20: Summary
To save the CPU cycles for IO
  Interrupt
  DMA
To access the device registers
  Memory-mapped IO
  Explicit IO instructions

## Slide 21
Hard Disk Drive (HDD)

## Slide 22: How does it work?
Physics, electro-magnetic field
https://www.youtube.com/watch?v=wteUW2sL7bc (physics)
https://www.youtube.com/watch?v=wtdnatmVdIg (components)

## Slide 23: Basic Geometry
Spindle
Disk arm
Disk head
Platter
Surface
Surface

## Slide 24: Basic Geometry (Cont.)
Track
Sector
(512 Byte)

## Slide 25: A Simple Disk Drive
Rotation Delay
If the full rotation delay is R,
the rotation delay of (30→24) is
RPM, rotations per minute
7200 to 15000 RPM
10000 RPM -> ~6ms per rotation

## Slide 26: A Simple Disk Drive (Cont.)
Seek Time
  To read sector 11
Phases of seek
Acceleration
→
Coasting
→
Deceleration
→
Settling time
(about 0.5~2 ms)
9

## Slide 27: A Simple Disk Drive (Cont.)
Cache (Track buffer)
30
22
10
4
27
…
Small amount of memory
(usually around 8 or 16MB)
Hold data read from or written to the disk
Allow the drive to quickly respond to requests

## Slide 28: A Simple Disk Drive (Cont.)
Cache (Track buffer)
30
22
10
4
27
…
Write-Back
Write-Through
Acknowledge the write has completed when it has put the data in its memory
Acknowledge after the write has actually been written to disk

## Slide 29: I/O Time: Doing The Math
I/O Time
I/O Rate

## Slide 30: I/O Time: Doing The Math (Cont.)
4KB Random Write Example
= 4ms
= 15,000 RPM(= 250RPS = 4ms / 1 rotation) / 2
= 2ms
= 4KB / 125(MB/s)
= 30us
= 4ms + 2ms + 30us ≒ 6ms
= 4KB / 6ms = 0.66MB/s

## Slide 31: I/O Time: Doing The Math (Cont.)
4KB Random Write Example (Cont.)
= 9ms
= 7,200 RPM(= 120RPS = 8ms / 1 rotation) / 2
= 4ms
= 4KB / 105(MB/s)
= 38us
= 9ms + 4ms + 38us ≒ 13ms
= 4KB / 13ms = 0.31MB/s

## Slide 32: I/O Time: Doing The Math (Cont.)
Sequential Write Example
= 4ms
= 15,000 RPM(= 250RPS = 4ms / 1 rotation) / 2
= 2ms
= 100MB / 125(MB/s)
= 800ms
= 4ms + 2ms + 800ms = 806ms ≒ 800ms
= 100MB / 800ms = 125MB/s

## Slide 33: I/O Time: Doing The Math (Cont.)
Sequential Write Example (Cont.)
= 9ms
= 7,200 RPM(= 120RPS = 8ms / 1 rotation) / 2
= 4ms
= 100MB / 105(MB/s)
= 950ms
= 9ms + 4ms + 950ms = 963ms ≒ 950ms
= 100MB / 950ms = 105MB/s

## Slide 34: I/O Time: Doing The Math (Cont.)
vs
Performance
Capacity
vs
Random Write
Sequential Write