## Slide 1: Operating Systems CSCI 3150
Lecture 10: Memory Management
Part I: Basics

## Slide 2: Overview
Address space, memory API
Address translation: Base and bound
Segmentation

## Slide 3
Memory API
Notes: In this lecture, we will explain the basic API’s that deal with the virtual memory.

## Slide 4: Overview
malloc/free
calloc/realloc
brk/sbrk
Notes: The API’s we are going to explain in this lsecture is …

## Slide 5: Virtual Address Space
Application
libc
Operating
System
malloc/free
brk/sbrk/mmap
mmap
(free)
Code
(Text)
Stack
Data
Heap
4KB
4KB
Heap
malloc()
free()
calloc()
realloc()
in libc
brk()
sbrk()
To manage the memory in a heap
To change the heap size
Notes: When a process is first created, it allocates the virtual address space for code, data heap and stack. In this picture, OS allocated 4 Kbyte pages for stack and heap respectively. A program uses malloc, free, calloc or realloc to manage the memory chunks within a heap. These functions are defined in libc. These functions are responsible for managing the virtual memory areas in the heap. There are a number of system calls that are used to adjust the isze of the virtual memory allocated to the process. These are system calls. They are brk/sbrk and mmap. Brk and sbrk are used to adjust the “break” point. “break” point is a end address of the heap.

## Slide 6: malloc()
Allocate a memory region on the heap.
  Argument
    size_t size : size of the memory block (in bytes)
    size_t is an unsigned integer type
  Return
    Success: a void type pointer to the memory block allocated by malloc
    Fail: a null pointer
#include <stdlib.h>
void* malloc(size_t size)
Notes: Malloc is defined in a libc library. It allocates a memorh region on the heap. It takes the size of a memory chunk that needs to allocated. When it succeeds, it returns the pointer to a memory chunk.

## Slide 7: sizeof()
Routines and macros are utilized for size in malloc instead typing in a number directly.
Two types of results of sizeof withvariables
  The actual size of ‘x’ is known at run-time.
  The actual size of ‘x’ is known at compile-time.
int *x = malloc(10 * sizeof(int));
printf(“%d\n”, sizeof(x));
4
int x[10];
printf(“%d\n”, sizeof(x));
40
Notes: Sizeof returns the size of a variable or the size of an object. There are two distinct usage as below. First, the sizeof function is used to return the size of an array. The return value of a sizeof function is determined at run time. Second, the size of ‘x’ is known at compile-time.

## Slide 8: Memory API: free()
Free a memory region allocated by a call to malloc
  Argument
    void *ptr : a pointer to a memory block allocated with malloc
  Return
    none
#include <stdlib.h>
void free(void* ptr)
Notes: The free() deallocates the memory chunk pointed by ptr. The ptr pointer should point to the address of the memory chunk allocated by malloc.

## Slide 9: Memory Allocating
int *pi; // local variable
(free)
stack
heap
*pi
2KB
pi = (int *)malloc(sizeof(int)* 4);
(free)
allocated
allocated
allocated
allocated
*pi
Address Space
Address Space
pointer
16KB
2KB
16KB
2KB + 4
2KB + 8
2KB + 12
Notes: Let us look at the exmaple. In this example, the stack starts from 16KByte and heap starts from 2 Kbyte. A program defines a local variable pi that is a pointer to integer. This pointer variable resides at the stack region.
The program called malloc (16). Then, the malloc function of libc allocates 16 byte from the heap. The malloc returns the address of the memory chunck it has allocated, 2 Kbyte.

## Slide 10: Memory Freeing
free(pi);
(free)
2KB(invalid)
freed
freed
freed
freed
*pi
(free)
2KB(invalid)
stack
heap
*pi
Address Space
Address Space
2KB
16KB
2KB + 4
2KB + 8
2KB + 12
16KB
2KB
Notes: Now, we call free(pi).
Then, the function free deallocates the memory object pointed by pi from the heap.

## Slide 11: System Calls
There lacks of heap space.  Ask OS to expand heap.
    break: The location of the end of the heap in address space
malloc uses brk system call.
  brk is called to expand the program’s break.
  sbrk is similar to brk.
  Programmers should never directly call either brk or sbrk.
#include <unistd.h>
int brk(void *addr)
void *sbrk(intptr_t increment);
(free)
Code
(Text)
Stack
Address Space
Data
Heap
4KB
4KB
brk()
sbrk()
To change the heap size
Operating System

## Slide 12
Address Translation
Notes: In this lecture, we will explain the basic API’s that deal with the virtual memory.

## Slide 13: Memory Virtualization with Efficiency and Control
Memory virtualization takes a similar strategy known as limited direct execution (LDE)
Efficiency and control are attained by hardware support.
  e.g., registers, TLBs (Translation Look-aside Buffers), page-table

## Slide 14: Address Translation
Hardware transforms a virtual address to a physical address.
  The desired information is stored in a physical address.
The OS must get involved at key points to set up the hardware.
  The OS must manage memory to judiciously intervene.

## Slide 15: Example: Address Translation
Code in C
  Load a value from memory
  Increment it by three
  Store the value back into memory
void func()
int x=3000;
...
x = x + 3; // this is the line of code we are interested in

## Slide 16: Example: Address Translation(Cont.)
Assembly
  Presume that the address of ‘x’ has been place in ebx register.
  Load the value at that address into eax register.
  Add 3 to eax register.
  Store the value in eax back into memory.
128 : movl 0x0(%ebx), %eax ; load 0+ebx into eax
132 : addl $0x03, %eax ; add 3 to eax register
135 : movl %eax, 0x0(%ebx) ; store eax back to mem

## Slide 17: Example: Address Translation (Cont.)
Fetch instruction at address 128
Execute this instruction (load from address 15KB)
Fetch instruction at address 132
Execute this instruction (no memory reference)
Fetch the instruction at address 135
Execute this instruction (store to address 15 KB)
(free)
3000
Stack
stack
heap
Heap
14KB
Program Code
16KB
15KB
0KB
1KB
2KB
3KB
4KB
128
132
135
movl 0x0(%ebx),%eax
Addl 0x03,%eax
movl %eax,0x0(%ebx)

## Slide 18: Dynamic Relocation (Hardware base): Base and Bounds
The OS wants to place the process somewhere in the physical memory, not at address 0.
  The address space start at address 0.
(free)
Stack
stack
heap
Heap
Program Code
16KB
0KB
(not in use)
(not in use)
Operating System
0KB
16KB
32KB
48KB
64KB
Code
(allocated but not in use)
Heap
Stack
Relocated Process
Address Space
Physical Memory

## Slide 19: Base and Bounds Register
(free)
Stack
stack
heap
Heap
Program Code
16KB
0KB
(not in use)
(not in use)
Operating System
0KB
16KB
32KB
48KB
64KB
Code
(allocated but not in use)
Heap
Stack
Address Space
Physical Memory
32KB
base register
16KB
bounds register

## Slide 20: Base and Bounds
When a program starts running, the OS decides where in physical memory a process should be loaded.
  Set the base register a value.
  Every virtual address must not be greater than bounds, or negative

## Slide 21: Relocation and Address Translation
  Fetch instruction at address 128
  Execute this instruction
    Load from address 15KB
(free)
3000
Stack
stack
heap
Heap
14KB
Program Code
16KB
15KB
0KB
1KB
2KB
3KB
4KB
128
132
135
128 : movl 0x0(%ebx), %eax
movl 0x0(%ebx),%eax
Addl 0x03,%eax
movl %eax,0x0(%ebx)
1KB = 1024B

## Slide 22: Two ways of Bounds Register
(free)
Stack
Heap
Program Code
16KB
0KB
(not in use)
(not in use)
Operating System
0KB
16KB
32KB
48KB
64KB
Code
(allocated but not in use)
Heap
Stack
Address Space
Physical Memory
48KB
16KB
bounds
bounds

## Slide 23: Hardware Requirements
Privileged mode: prevent user-mode processes from executing privileged operations
Base/bounds registers: Need a pair of registers per CPU to support address translation and bounds checks
Ability to translate virtual addresses and check if within bounds limits; Circuitry to do translations.
Privileged instruction(s) to update base/bounds: OS must be able to set these values before letting a user program run
Privileged instruction(s) to register: OS must be able to tell hardware what exception handlers code to run if exception occurs
Ability to raise exceptions when processes try to access privileged instructions or out-of-bounds memory

## Slide 24: OS Issues for Memory Virtualization
The OS must take action to implement base-and-bounds approach.
Three critical junctures:
  When a process starts running:
    Finding space for address space in physical memory
  When a process is terminated:
    Reclaiming the memory for use
  When context switch occurs:
    Saving and storing the base-and-bounds pair

## Slide 25: OS Issues: When a Process Starts Running
The OS must find a room for a new address space.
  free list : A list of the ranges of physical memory which are not in use.
0KB
16KB
32KB
48KB
64KB
Code
(allocated but not in use)
Physical Memory
The OS lookup the free list
(not in use)
Heap
Stack
Operating System
(not in use)
Free list
16KB
48KB

## Slide 26: OS Issues: When a Process Is Terminated
The OS must put the memory back on the free list.
Operating System
0KB
16KB
32KB
48KB
64KB
Physical Memory
(not in use)
(not in use)
Operating System
0KB
16KB
32KB
48KB
64KB
Physical Memory
(not in use)
(not in use)
(not in use)
Process A
Free list
16KB
48KB
Free list
16KB
32KB
48KB

## Slide 27: OS Issues: When Context Switch Occurs
The OS must save and restore the base-and-bounds pair.
  In process structure or process control block (PCB)
Operating System
0KB
16KB
32KB
48KB
64KB
Physical Memory
(not in use)
Process A
Currently Running
Process B
48KB
bounds
32KB
base
Context Switching
Operating System
0KB
16KB
32KB
48KB
64KB
Physical Memory
(not in use)
Process A
Process B
Currently Running
64KB
48KB
Process A PCB
…
base : 32KB
bounds : 48KB …
bounds
base

## Slide 28
Segmentation
Notes: In this lecture, we will explain the basic API’s that deal with the virtual memory.

## Slide 29: Inefficiency of Base and Bounds
Big chunk of “free” space
“free” space takes up physical memory
Hard to run when an address space does not fit into physical memory
(free)
14KB
Program Code
16KB
0KB
2KB
4KB
Heap
Stack
6KB
15KB
5KB
3KB
1KB

## Slide 30: Segmentation
A segment is just a contiguous portion of the address space of a particular length
  Logically different segments: code, stack, heap
Each segment can be placed in different parts of the physical memory
  Base and bounds exist for each segment

## Slide 31: Placing Segments in Physical Memory
0KB
16KB
32KB
48KB
64KB
Code
Physical Memory
(not in use)
(not in use)
Heap
Stack
Operating System
(not in use)
Segment Base Size
Code 32K 2K
Heap 34K 2K
Stack 28K 2K

## Slide 32: Address Translation with Segmentation: code
The offset of virtual address 100 is 100.
  The code segment starts at virtual address 0 in address space.
Segment Base Size
Code 32K 2K
0KB
2KB
Program Code
4KB
16KB
32KB
100
instruction
Heap
Code
(not in use)
(not in use)
34KB
is the desired physical address

## Slide 33: Address Translation on Segmentation: heap
The offset of virtual address 4200 is 104 (4200-4096)
  The heap segment starts at virtual address 4096 in address space.
Segment Base Size
Heap 34K 2K
32KB
Heap
Code
(not in use)
(not in use)
34KB
is the desired physical address
6KB
Heap
4KB
Address Space
Physical Memory
4200
data
36KB
is not the correct physical address.
(Offset of v is the correct physical address.

## Slide 34: Segmentation Fault or Violation
If an illegal address such as 7KB which is beyond the end of heap is referenced, the OS occurs segmentation fault.
  The hardware detects that address is out of bounds.
6KB
Heap
4KB
(not in use)
Address Space
7KB
8KB

## Slide 35: Referring to A Segment
Explicit approach
  Chop up the address space into segments based on the top few bits of virtual address
Example: virtual address 4200 (01000001101000)
0
13
1
12
2
11
3
10
4
9
8
7
6
5
Segment
Offset
0
13
1
12
2
11
3
10
4
9
8
7
6
5
Segment
Offset
0
0
0
1
0
0
1
0
0
0
0
0
1
1
Segment bits
Code 00
Heap 01
Stack 10
- 11

## Slide 36: Segment selection
  SEG_MASK = 0x3000(11000000000000)
  SEG_SHIFT = 12
  OFFSET_MASK = 0xFFF (00111111111111)
1 // get top 2 bits of 14-bit VA
2 Segment = (VirtualAddress & SEG_MASK) >> SEG_SHIFT
3 // now get offset
4 Offset = VirtualAddress & OFFSET_MASK
5 if (Offset >= Bounds[Segment])
6 RaiseException(PROTECTION_FAULT)
7 else
8 PhysAddr = Base[Segment] + Offset
9 Register = AccessMemory(PhysAddr)

## Slide 37: Referring to the Stack Segment
Stack grows backwards
Extra hardware support is need
  The hardware checks which way the segment grows.
  1: positive direction, 0: negative direction
Segment Base Size Grows Positive?
Code 32K 2K 1
Heap 34K 2K 1
Stack 28K 2K 0
Stack
(not in use)
(not in use)
28KB
26KB
Physical Memory
Segment Registers (with Negative-Growth Support)

## Slide 38: Support for Sharing
Segment can be shared between address spaces
  Code sharing is still in use in systems today
Extra hardware support is need for form of Protection bits.
  A few more bits per segment to indicate permissions of read, write and execute
Segment Base Size Grows Positive? Protection
Code 32K 2K 1 Read-Execute
Heap 34K 2K 1 Read-Write
Stack 28K 2K 0 Read-Write
Segment Register Values (with Protection)

## Slide 39: OS support: Fragmentation
External Fragmentation: little holes of free space in physical memory that may be individually too small for segment
  There is 24KB free, but not in one contiguous segment.
  The OS cannot satisfy a 20KB request
Compaction: re-arranging the exiting segments
  Compaction is costly
    Stop running processes
    Copy data to somewhere
    Change segment register values

## Slide 40: Memory Compaction
0KB
16KB
32KB
48KB
64KB
Not compacted
Operating System
8KB
24KB
40KB
56KB
Allocated
(not in use)
0KB
16KB
32KB
48KB
64KB
Operating System
8KB
24KB
40KB
56KB
(not in use)
(not in use)
Allocated
(not in use)
Allocated
Allocated
Compacted

## Slide 41: Issues of Segmentation
External fragmentation
Still inefficient and inflexible, when a segment is only sparsely used
Better solution? Yes!

## Slide 42: History of segmentation
In the early days, OS used segmentation
  Burroughs B5000 (first commercial machine with virtual memory)
  IBM AS/400
  Intel 8086, 80286
80386 and later Intel CPUs support paging
X86-64 does not use segmentation any more in 64-bit mode
  CS,SS,DS and ES are forced to 0 and 2^24