## Slide 1: Operating Systems
Lecture 16: File Systems
Part IV: Solid-State Drive

## Slide 2: Solid-State Drive vs. Hard Disk Drive (SSD vs. HDD)
SSD’s advantages:
  Faster performance
  No vibrations or noise; shock-resistance
  Lighter, smaller

## Slide 3: Overview
Solid-state storage device
  No mechanical or moving parts like HDD.
  Built out of transistors (like memory and processors).
  Retain information despite power loss unlike typical RAM.
NAND Flash based SSD
  To write to a given chunk of it, you have to erase a bigger chunk.
  The number of erase/write is limited.

## Slide 4: Storing Bits
Single-level cell (SLC): a single bit per cell
Multi-level cell (MLC): two bits per cell
Triple-level cell (TLC): three bits per cell
QLC, PLC
Flash memory
cell

## Slide 5: Structure of Flash
Data area
Spare area
Page
block
Flash cells -> Pages
Pages-> Blocks

## Slide 6: Structure of Flash SSD

## Slide 7: Asymmetric Operation Units
Read; Write (program): 1  0: in page unit.
Erase: 0  1: in block unit
Write-once property: A flash page cannot be overwritten until the residing block is erased first.
1
1
1
1
1
1
1
1
1
1
0
0
1
1
0
0
1
1
0
0
0
0
0
0
1
1
1
1
1
1
1
1
Write 0xCC
(11001100)
Write 0xF0
(11110000)
Erase block
Initial status
Initial status
Can’t write
write
Erase
Block
Block
Block
1010101010101
1010101010101
1111111111111
1010001011101
1010001011101
1111111111111
1111111111111
0000101110100
1111111111111
1111111111111
1111111111111
1111111111111

## Slide 8: Reliability of Flash
Wear out
  Flash cells wear out as we program/erase it (P/E cycles)
  Eventually the block becomes unusable.
  Typical erase/wear out cycle
    MLC-based block: 10,000 P/E cycles
    SLC-based block: 100,000 P/E cycles
Disturbance
  When accessing a page, it is possible that some bits in the neighboring pages get flipped (interference)
  It is called read disturbance or program disturbance.

## Slide 9: Out-of-place update in Flash memory
Flash memory should be erased before written.
Flash SSD uses out-of-place update for write operation.
sector 0
sector 2
sector 3
sector 4
sector 5
sector 0
sector 1
sector 2
sector 3
sector 4
sector 5
write sector 1
sector 0
sector 1
sector 2
sector 3
sector 4
sector 5
write sector 1
sector 1
1
Block 1
Block 1
Block 1
In-place
out-of-place
sector 1

## Slide 10: System Architecture
There are two typical ways to address the inherent challenges of flash memory
  Implementing a flash translation layer in the device
  Designing a flash-aware file system in the host

## Slide 11: Flash Translation Layer
Software that makes the SSD look like HDD
  Address translation
    Program pages within an erased block in order (from low page to high page)
  Wear leveling
    FTL should try to spread writes across the blocks of the flash
    Ensuring that all of the blocks of the device wear out at roughly the same time.
  Garbage collection

## Slide 12: Hard Disk and Flash SSD
+
Device Driver
Read
Write
Erase
File System
Read Sectors
Write Sectors
Flash Memory
Flash Memory
Mismatch!
+
Device Driver
Read Sectors
Write Sectors
File System
Read Sectors
Write Sectors

## Slide 13: Flash Translation Layer
Append the write to the next free spot in the currently-being-written-to block.

## Slide 14: Example
Assume that a page size is 4 Kbyte and a block consists of four pages.
Write(page number)
  Write(100) with contents a1
  Write(101) with contents a2
  Write(2000) with contents b1
  Write(2001) with contents b2
The initial state of SSD, with all pages marked INVALID(i).

## Slide 15: Example
Erase block 0.
Program pages in order and update mapping information (logical block address to physical page address)
After performing four writes.

## Slide 16: Garbage collection
Update the existing page  old version of data becomes obsolete.
Update logical blocks 100 and 101 with contents c1 and c2.
The pages 0 and 1 in block 0 is old version data and these are called garbage.
These garbage pages must be reclaimed for new writes to take place.
Garbage

## Slide 17: Address Translation
Page 29
Block 125
Map
(#125, #29)
Sec #3045
write
Page 29
Block 125
Page 4
Block 237
Map
(#237, #4)
Sec #3045
Not Used
Block 125
Page 4
Block 237
update

## Slide 18: Garbage collection
the process of finding garbage blocks and reclaiming them.
Basic process
  Find a block that contains one or more garbage pages.
  Read in the live(non-garbage) pages from that block.
  Write out those live pages to the next writable pages.
  Reclaim the entire block for use in writing.

## Slide 19: Garbage collection
Update request
for existing data
Block (A)
Find a free page,
and save the new data
Block (A)
New Data
Invalid
This scenario may continue until there
are not enough free blocks
Block (A)
Invalid
Block (B)
Invalid
Block (C)
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Collect valid pages into a free block
Block (A)
Invalid
Block (B)
Invalid
Block (C)
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Update the map table, and
erase invalid (obsolete) blocks
Block (A)
Block (B)
Block (C)

## Slide 20: Garbage collection
Garbage collection is expensive
  Require reading and rewriting of live data.
  Ideal garbage collection is reclamation of a block that consists of only dead pages.
Cost of Garbage Collection
  Amount of data blocks that are migrated.
  Overprovision the device by adding extra flash capacity Cleaning can be delayed.
  Run the GC in the background.

## Slide 21: Mapping Table Size
Size of page-level mapping table is too large
  With a 1TB SSD with a 4byte entry per 4KB page, 1GB of DRAM is needed for mapping.
Some approaches to reduce the costs of mapping
  Block-based mapping
  Hybrid mapping
  Page mapping plus caching

## Slide 22: Block Mapping
Mapping at block granularity.
  To reduce the size of a mapping table.
Small write problem: When a small write occurs, the FTL must read a large amount of live data from the old block and copy them into a new one.
Logical blocks 2000, 2001, 2002, and 2003 are at the same Flash block (500), and have different offsets (0, 1, 2, and 3).
The FTL records that chunk 500 maps to block 0.

## Slide 23: Example
If the logical block 2002 is updated with contents c’,
  FTL must read in 2000, 2001, and 2003.
  Write out all four logical blocks in a new location.
  Update the mapping table.

## Slide 24: Hybrid mapping
In hybrid mapping, FTL maintains
  Log blocks: page-mapped
  Data blocks: block-mapped
Write to log blocks first
When looking for a particular logical block, the FTL will consult the page mapping table and block mapping table in order.
valid
valid
valid
valid
Write!
Data is written to
the log block
Data Block
Log Block

## Slide 25: Example
In the following situation,
Update these pages (with data a’, b’, c’, and d’).  write them to the log block. FTL updates the page mapping information.

## Slide 26: Switch Merge
When log block is full, perform merge.
  Switch merge

## Slide 27: Switch Merge
valid
valid
valid
valid
valid
valid
valid
valid
Free blocks
Data Block
Data Block
Log Block

## Slide 28: Partial Merge
Client overwrites logical block 1000 and 1001 partially. What happened?
The FTL writes logical block 1000 and 1001(contents a’ and b’) to the available pages in new block.
And then, the FTL appends other live data.

## Slide 29: Partial Merge
valid
valid
valid
valid
valid
valid
valid
valid
Free blocks
Data Block
Log Block
Free Block

## Slide 30: Switch and Merge

## Slide 31: Page mapping plus caching
Caching only the active part of the page-mapped FTL in memory.
  If a given workload only accesses a small set of pages, the translations of those pages will be stored in the in-memory FTL.
Performance will be excellent without high memory cost.
Cache miss overhead exists.
Page mapping table
Memory
1000 → 0
1001 → 1
1002 → 2
1003 → 3
1004 → 4
1005 → 5
Working set

## Slide 32: Wear Leveling
Program/Erase cycle is limited in Flash memory.
If P/E cycle is skewed, that shortens the lifespan of the entire Flash storage.
All blocks should wear out at roughly the same time.
A block may consist of cold data.
  The FTL must periodically read all the live data out of such blocks and re-write it elsewhere.
  Wear leveling increases the write amplification of the SSD and decreases performance.
Sample Policy: Each Flash Block has a P/E cycle counter.
  Maintain |Max(PE cycle) – Min(PE cycle)| < e
  Maintain |Max(PE cycle) – Min(PE cycle)|/Max(PE cycle) < e
X
O

## Slide 33: Summary
Flash-based SSDs are a common presence in …
  laptops, desktops, and servers inside the datacenters.
Flash Translation Layer
  Address Translation
  Wear Leveling
  Garbage Collection